## Slide 1
Experimental setup
Cryostat thermal simulator — what was held fixed, and at what value
Plant & model | 
Graph | 2.99 M cells · 27 heaters · 27 sensors
Gain G | exact DC solve of L T = P
Linearised at | T_op = 50 K
Conditioning | cond 366 · σ₁ = 81 % of the plant
Properties | k(T), c_p(T) ___
Radiation | to ambient only — no view factors
Solver | implicit step, GPU conjugate gradient
Conservation | energy drift ~1e−6 throughout
Controller & run | 
Scheme | static-decoupling MIMO PI
Allocation | bounded least squares, u ≥ 0
Gains | K_p = 5.5 · K_i = ___
Filter | τ_f = 900 s, feedback path only
Step size | dt = ___ s
Heater limit | ___ W each
Setpoints | ___ K, uniform across sensors
Channels | 25 of 27 in the loop — 2 unreachable
Initial state | uniform at ___ K
Duration | 27.8 h ≈ 1.2 × dominant time constant
Notes: Amber entries are still placeholders: pull dt, K_i, the heater limit, the setpoint and the initial temperature from the run's simulation_parameters.json before presenting. The heater limit especially — the saved parameter says 1.5 W per heater while the talk quotes 7-11 W of 30, and those cannot both be right.